## Slide 1
VSM ENGINEERING · FEASIBILITY STUDY
RoboSprayer Electric
Deterministic feasibility study on a validated 347-sample electric field profile.
GVW 3,500 kg
Electric powertrain
12 kph field
Battery 50 kW
Motor 63 rpm
DISTANCE
1.00 km
MISSION TIME
5.77 min
FINAL BATTERY SOC
72.45 %
ENERGY CONSUMPTION
3,778.1 Wh/km
RANGE @ 85%
11.25 km
MAX BATT POWER
47.92 kW
Samples: 347 | Tool version: v1.3.0
1 / 10

## Slide 2
System & Simulation Overview
Electric profile resolution and deterministic simulation scope
GVW 3,500 kg
Electric powertrain
12 kph field
Battery 50 kW
Motor 63 rpm
Mission Structure
▸ Selected reporting profile: Electric.
▸ Powertrain type: fully electric.
▸ Imported samples: 347 · source channels: 601.
▸ Resolved required raw channels: 289 / 289.
Computation Context
▸ Calculated MATH channels: 25.
▸ Calculated statistics: 27 · KPIs: 9.
▸ Rendered profile plots: 14.
▸ Inactive / all-zero resolved channels: 33.
MISSION TIME
5.77 min
DISTANCE
1.00 km
MAX SPEED
14.93 kph
FINAL BATTERY SOC
72.45 %
VSM ENGINEERING · POST-PROCESSING TOOL v1.3.0
2 / 10

## Slide 3
Executive Results
Deterministic KPIs from the validated profile pipeline
● Battery ● Consumption ● Mission
MISSION TIME
5.77 min
DISTANCE
1.00 km
MAX SPEED
14.93 kph
INITIAL BATTERY SOC
80.00 %
FINAL BATTERY SOC
72.45 %
BATTERY CAPACITY USED
3.77 kWh
ENERGY CONSUMPTION
3,778.1 Wh/km
RANGE @ 85%
11.25 km
Calculations are sourced from the profile statistics and KPI results.
VSM ENGINEERING · POST-PROCESSING TOOL v1.3.0
3 / 10

## Slide 4
Vehicle Operation
Speed trace from the validated profile plot output
DISTANCE
1.00 km
MISSION TIME
5.77 min
MAX SPEED
14.93 kph
FINAL BATTERY SOC
72.45 %
VSM ENGINEERING · POST-PROCESSING TOOL v1.3.0
4 / 10

## Slide 5
Battery & Electrical Energy System
State of charge, stored energy and battery demand
INITIAL BATTERY SOC
80.00 %
FINAL BATTERY SOC
72.45 %
MAX BATT POWER
47.92 kW
BATT POWER RMS
36.78 kW
HEATFLOW RMS
3.64 kW
BATTERY CAPACITY USED
3.77 kWh
VSM ENGINEERING · POST-PROCESSING TOOL v1.3.0
5 / 10

## Slide 6
Battery Power & Energy Recovery
Charge / discharge behaviour and released / recuperated energy
BATT POWER RMS
36.78 kW
ENERGY RELEASED
1.80 kWh
ENERGY RECOVERED
0.00 kWh
AUX ENERGY
1.04 kWh
MAX BATT POWER
47.92 kW
VSM ENGINEERING · POST-PROCESSING TOOL v1.3.0
6 / 10

## Slide 7
Energy Consumption & Estimated Range
Battery energy consumption and range indicators
BATTERY CAPACITY USED
3.77 kWh
ENERGY CONSUMPTION
3,778.1 Wh/km
RANGE @ 85%
11.25 km
FINAL BATTERY SOC
72.45 %
MAX BATT POWER
47.92 kW
AUX ENERGY
1.04 kWh
Range and consumption are deterministic profile KPI outputs.
VSM ENGINEERING · POST-PROCESSING TOOL v1.3.0
7 / 10

## Slide 8
Agrochemical & Battery Behaviour
Profile-supported system interaction from the active source data
AGRO DISCHARGE
499.83 kg
FINAL BATTERY SOC
72.45 %
BATTERY CAPACITY USED
3.77 kWh
MISSION TIME
5.77 min
VSM ENGINEERING · POST-PROCESSING TOOL v1.3.0
8 / 10

## Slide 9
Traction, EDU & Auxiliary Energy Demand
Wheel, EDU, tyre and auxiliary demand from profile plots
EDU MECH POWER
25.34 kW
WHEEL POWER
0.00 kW
EDU SPEED RL
70 rpm
EDU TORQUE RL
1,420.9 Nm
TYRE RR ENERGY
1.24 kWh
AUX ENERGY
1.04 kWh
VSM ENGINEERING · POST-PROCESSING TOOL v1.3.0
9 / 10

## Slide 10
Simulation Summary
Deterministic profile result snapshot
1.00 km covered · SOC 72.45 % · consumption 3,778.1 Wh/km
DETERMINISTIC SUMMARY
▸ Deterministic run covered 1.00 km in 5.77 min.
▸ Final battery SOC is 72.45 % from an 80.00 % initial state.
▸ Battery capacity used is 3.77 kWh; estimated range for 85% battery is 11.25 km.
▸ Results are deterministic simulation outputs; acceptance conclusions require explicit engineering criteria.
DISTANCE
1.00 km
MISSION TIME
5.77 min
FINAL BATTERY SOC
72.45 %
BATTERY CAPACITY USED
3.77 kWh
ENERGY CONSUMPTION
3,778.1 Wh/km
RANGE @ 85%
11.25 km
VSM ENGINEERING · POST-PROCESSING TOOL v1.3.0
10 / 10